## Slide 1: IP Protocols and IP Address
PRESENTED BY:
SEGU RASOOL
NELLORE GUNA SHEKAR

## Slide 2: IP Protocols and IP Address
The Internet Protocol (IP) is one of the most important protocols used in computer networks. It helps deliver data packets between devices across networks. IP operates in the Network Layer (Layer 3) of the OSI model and defines addressing and routing of data.

## Slide 3: What is an IP Address?
An IP Address (Internet Protocol Address) is a unique numerical label assigned to each device connected to a network. It identifies and locates devices and allows communication between them.
Examples:
IPv4 → 192.168.1.10
IPv6 → 2001:0db8:85a3::8a2e:0370:7334
Just like a house address helps deliver letters, an IP address helps route data to the correct device.

## Slide 4: Structure of an IP Address
An IP address has two parts:
• Network ID – Identifies the network.
• Host ID – Identifies the device in that network.
Example: 192.168.10.5 → Network ID: 192.168.10 | Host ID: 5
Routers use the network part to forward packets to the correct destination.

## Slide 5: IPv4 (Internet Protocol version 4)
IPv4 is a 32-bit numeric addressing system written in dot-decimal notation.
Each octet ranges from 0 to 255.
Example: 172.16.0.1
IPv4 supports around 4.3 billion addresses. Due to the huge growth of the Internet, these addresses are nearly exhausted.

## Slide 6: Classes of IPv4 Addresses
IPv4 addresses are divided into five classes based on network size:
Class A: 1.0.0.0 – 126.255.255.255 → Large Networks
Class B: 128.0.0.0 – 191.255.255.255 → Medium Networks
Class C: 192.0.0.0 – 223.255.255.255 → Small Networks
Class D: 224.0.0.0 – 239.255.255.255 → Multicasting
Class E: 240.0.0.0 – 255.255.255.255 → Experimental use

## Slide 7: IPv6 (Internet Protocol version 6)
IPv6 is a 128-bit addressing system designed to replace IPv4.
It uses hexadecimal numbers and colons (:) to separate groups.
Example: 2001:0db8:0000:85a3:0000:0000:ac1f:8001
IPv6 provides an enormous number of addresses, improved routing efficiency, and built-in security (IPSec).

## Slide 8: Difference Between IPv4 and IPv6
Feature | IPv4 | IPv6
Address Length | 32-bit | 128-bit
Format | Decimal | Hexadecimal
Addresses | 4.3 Billion | Trillions
Security | Optional IPSec | Built-in IPSec
Header | Simple | Complex but efficient

## Slide 9: Types of IP Addresses
1. Public IP – Used on the Internet, assigned by ISPs.
2. Private IP – Used inside local networks (e.g., 192.168.x.x).
3. Static IP – Fixed address, manually assigned (used for servers).
4. Dynamic IP – Changes automatically via DHCP (used by most users).

## Slide 10: IP Protocol Overview
The Internet Protocol (IP) is connectionless and unreliable by itself. It does not guarantee delivery or order of packets but ensures correct addressing and routing.
Reliability is managed by higher-layer protocols such as TCP (Transmission Control Protocol).

## Slide 11: Important IP Protocols
• ICMP (Internet Control Message Protocol) – Used for error reporting and diagnostics (e.g., ping).
• ARP (Address Resolution Protocol) – Finds MAC address for a given IP.
• RARP (Reverse ARP) – Finds IP from a MAC address.
• IGMP (Internet Group Management Protocol) – Manages multicast groups.
• IPSec (Internet Protocol Security) – Provides secure IP communication.

## Slide 12: Functions of IP
1. Addressing – Assigns unique identifiers to each device.
2. Routing – Determines the best path for packets.
3. Fragmentation & Reassembly – Breaks and rebuilds data packets.
4. Encapsulation – Wraps higher-layer data for transmission.
5. Error Handling – Works with ICMP for control messages.

## Slide 13: How IP Works (Step-by-Step)
1. Data is generated by the Application Layer.
2. The Transport Layer adds port numbers (TCP/UDP).
3. The Network Layer (IP) adds source and destination IP addresses.
4. Packets travel through routers to the destination.
5. At the destination, packets are reassembled and delivered to the correct process.

## Slide 14: Importance of IP Protocols
• IP forms the foundation of the Internet.
• Enables inter-device communication across networks.
• Provides secure and efficient data transfer.
• Essential for network engineers and cybersecurity professionals.

## Slide 15: Real-Life Example
When you visit a website:
1. Your browser requests the IP of the site via DNS.
2. Your computer sends data packets from its IP to the server’s IP.
3. IP routes them through routers to reach the server.
4. The server sends back webpage data using your IP address.
This entire process depends on IP addressing and routing.

## Slide 16: Conclusion
• IP and its associated protocols are the backbone of Internet communication.
• Every online activity depends on IP addressing and routing.
• Understanding IP helps in mastering computer networks, cybersecurity, and ethical hacking.
Quote: “No IP – No Internet!”